## Slide 1: BLE SMART VENTS
Notes: It is using the background from https://dribbble.com/shots/1588545--Freebie-7-Low-Poly-Backgrounds-svg-png
Template modified by fppt.com

## Slide 2: INTRODUCTION
The goal was to give homeowners:
  more control over how their heating & cooling systems
  an increase in the efficiency & effectiveness of traditional HVAC systems
  a design utilizing for systems using a singular furnace.

## Slide 3: TECHNOLOGY
A smart vent includes:
  standard-sized vent registers (4″x10″)
  bluetooth-capable microcontroller (RSL15 development board from Onsemi)
  temperature & humidity sensors (Mikroe-3436 HDC2080)
  a motor-controlled closing mechanism (FS90 Servo motor).

## Slide 4: METHODOLOGY
These Vents connect to the central Hub unit, which maintains the system through the user- directed schedule and provides a GUI dashboard for system monitoring.

## Slide 5: METHODOLOGY

## Slide 6: METHODOLOGY
A humidity sensor and a temperature sensor are integrated into HDC2080 device which is controlled by RSL15 over I2C communication.
Bluetooth has been used for the connection of mobile application from hub to vent unit.

## Slide 7: METHODOLOGY

## Slide 8: METHODOLOGY
The servo motor controlling opening/closing mechanism can be done by using PWM peripheral function.

## Slide 9: METHODOLOGY

## Slide 10: METHODOLOGY
For the hub unit, python has been used to perform the operation over raspberry pi.

## Slide 11: RESULTS
In our tests, we used a small single-vented bathroom to maintain the room temperature at 22°C with a hysteresis of 1°C, and collected three sets of data over of three days.
  For the first set of data, we opened the vent register fully and left it open, collecting temperature readings at 1-minute intervals for 24 hours.
  For the second set, we closed the vent register fully and again collected temperature readings for 24 hours at 1-minute intervals.
  And for the third set of data, we again collected data at 1-minute intervals for 24 hours; however, for this set, we used our automated Vent unit to open and close the vent throughout the collection period.

## Slide 12: RESULTS